Project:  To the moon!

Your team has been tasked to design the mission parameters for the RANGER X lunar mission.  Several other teams have been tasked with the same mission.  The team that has the best mission plan will be selected for the contract to build the Ranger X mission.

The original Ranger 7 mission in 1964 was tasked with launching a satellite from the Earth to the Moon in order to photograph the moon. The Ranger X mission will leave earth and orbit the moon with goal of producing a detailed orbital photographic and mineral survey for the location of a new moon base to support lunar mining activities.  Your satellite will have the same fuel, mass and thrust profile as the original ranger satellite.  Note that 1 kg of fuel with produce 1000Ns of thrust.

To send a spacecraft to the Moon, we put it on top of a large rocket containing lots of rocket fuel and fire it upward. At first the huge ship moves quite slowly, but the speed increases rapidly. When the "first-stage" portion of the rocket has exhausted its fuel and is empty, it is discarded and falls back to Earth. By discarding an empty rocket stage we decrease the amount of mass that must be accelerated to even higher speeds. There may be several stages that operate for a while and then are discarded before the spacecraft has risen above most of Earth's atmosphere (about 50 km, say, above the Earth), and has acquired a stable orbit around the earth. At this point a thruster is fired and the satellite must transfer from its earth orbit to the moon.  Once the satellite reaches the moon, it must again fire its thruster and enter the moons orbit at a height of 20 km.  At this point all the fuel available for this mission has been used up, and the spacecraft simply orbits the Moon through the vacuum of space.

Factors that would certainly influence the path of the spacecraft include the motion of the Moon around the Earth, and the motion of the Earth around the Sun. In addition, the Sun and other planets exert gravitational forces on the spacecraft. You must include these additional factors as part of your mission profile.

The best mission profile will be judged based on the following formula:

SCORE = Fuel Consumed in kg * 100 + mission time in seconds/100.

The lowest scoring mission will be selected as the NASA contractor for this project.

The following are required for your mission profile:

1.  Working computational model of the RANGER X mission.

- visual representation of the satellite leaving earth orbit, traveling to the moon and entering lunar orbit.

- output of fuel consumed during each thrust and total time elapsed from leaving earth orbit until reaching lunar orbit.

2.  10 minute powerpoint presentation about your mission design, explaining the internal details of your model.

HINT: You will want to do some research about the original ranger mission and the later missions that actually orbited the moon.  BTW the Chinese government has decided to launch as lunar orbital mission (Chang'e No.1)  by the end of 2007 so folks in China will be busy doing these same calculations!

The project will be due Wednesday 9-28.